## Slide 1
Arduino Leonardo, Micro or ProMicro
Wiring diagram for optical quadrature encoder and FFB clip LED (valid for all firmware versions)
Any 5V optical quadrature encoder
max supported PPR=10k
Arduino Encoder
GND 0V, shield
5V VCC or 5V
TX A+
RX B+
2 Z+
Internal 100k pullup resistors are
enabled in firmware, but you may
want to add additional ones in order
to avoid step skipping which manifest
as losing of wheel center over time,
anything between 1K and 4.7K is ok
5V DC
0V (common)
GND (shield)
OUT A
OUT B
OUT Z
3x 3.3K
FFB clip LED indicator function
FFB (%)
LED intensity (%)
0
90
100
50
100
Arduino FFB clip LED pin
Leonardo, Micro 13
ProMicro 3 (fw option “m”)
FFB clip LED is not just a simple ON/OFF
indicator, it turns on at half brightness
for 90% of FFB, while for last 10% of FFB
it has linearly increasing intensity
up to a full brightness level
giving you ability to easily fine tune
FFB strength and get the most details
220R
OMRON E6B2-CWZ1X