## Slide 1
Arduino Leonardo, Micro or ProMicro
Wiring diagram for H-bridge motor driver (valid for all firmware in PWM± mode, except fw-vXX3)
B-
B+
M+
M-
BTS7960 or any other 2 channel H-bridge
motor driver with PWM inputs
Standard pinouts:
Arduino BTS7960 (pin)
GND GND (8)
5V VCC (7), R_EN (3), L_EN (4)
9 LPWM (2)
10 RPWM (1)
BTS7960 pins:
B+, B- DC power supply input (5.5-27)V
M+, M- DC motor output (max 300W)
R_IS, L_IS are current shunt outputs
that may be used for monitoring
current load at each channel, but you
have to connect a shunt resistor to each
If your motor is very hard to turn
by hand when there is no PWM
signal input, then you may
try the wiring trick by shorting
BTS pins VCC, R_EN, L_EN
together and leave them floating!
* floating means not connected
anywhere (no voltage on them)
1k
R_IS, L_IS
Vout
(0-5)V -> (0-43)A
*